## Slide 1: Development of a new Python-based cardiac phantom for myocardial SPECT imaging

## Slide 2: What is SPECT?
Single Photon Emission Computed Topography
Helps in cardiac imaging
Notes: SPECT is a type of nuclear imaging test that shows how blood flows to tissues and organs
Myocardial Perfusion SPECT specifically used to evaluate blood flow to the heart muscle
Helps in diagnosing various heart conditions, such as coronary artery disease, and assessing heart muscle damage after a heart attack
Simulated Gated myocardial Perfusion SPECT simulates the heart’s pumping action (gating) to provide detailed images of the heart’s blood flow during different phases of the heart beat

## Slide 3: Anthropomorphic Human Phantoms
Objects that simulate human tissues and organs to test and calibrate imaging devices
Used in nuclear medicine
  Image acquisition
  Reconstruction
  Data analysis
  Calibration, etc

## Slide 4: Types of Phantoms
Numerical Phantoms
  Stylized Phantoms: Use mathematical equations to represent human anatomy
    Analytical geometries
  Voxel Phantoms: Use 3D imaging techniques like MRI or CT scans
    More realistic, derived from human patients
Non-numerical phantoms
  Physical models

## Slide 5: Quantitative Measurements
End Diastolic Volume(EDV)
  Volume of blood in the left ventricle at the end of filling
End-Systolic Volume (ESV)
  Volume of blood in the left ventricle after contraction
Ejection Fraction(EF)
  Percentage of blood pumped out of the left ventricle during each heartbeat
Phase Analysis, Wall Thickening Motion, Perfusion Parameters
  Various measures of heart function and blood flow
Defect Extent and Severity, Stress and Rest Scores, Total Perfusion Deficit(TPD)
  Assessment of areas with poor blood flow and overall heart health
Notes: There are numerous software programs that are used to derive quantitative information from gated myocardial perfusion SPECT. Some of these measurements include:

## Slide 6: The Problem
Current Cardiac Phantoms limited in realism and flexibility
Stylized Phantoms lack detail of anatomical model
Voxel Phantoms are rigid and less flexible

## Slide 7: Study Aim
Design a computational cardiac phantom
  Simulate interfering Parameters
  Accurate phantom for validating and improving the quantitative analysis software
Computational Phantom
  Versatile
  Enhanced Accuracy

## Slide 8: Why use Python?
High-Level programming language
Easy Syntaxes
Flexibility
More advantages over other languages

## Slide 9: Python Libraries Used
NumPy: handling large datasets
SciPy:

## Slide 10: Results

## Slide 11: Results

## Slide 12: My Thoughts

## Slide 13: References

## Slide 14: Questions